## Slide 1
We will compare three MediaPipe pose models on the Arduino UNO Q, first on video, then on a live webcam
WHAT IS COMPARED
Pose Landmarker Lite, Full and Heavy. Same 33 landmarks, different size and accuracy.
Left out on purpose:
• The older mp.solutions.pose: unsupported since 2023 and has no build for the Board's Python 3.13.
• Arduino's PoseNet brick: not MediaPipe, 17 keypoints, restricted to the VENTUNO Q.
TWO PHASES
1. Video phase. Every variant runs on the Board over the same five stock Clips: front view, side view, fast movement, far away or partly hidden, empty room. Each pairing runs 3 times.
2. Webcam phase. Only variants that pass move on to the Logitech Brio 105 at 1280x720: three 60 second sessions each.
If no variant passes, that is the finding, and the webcam demo runs Lite only, labelled as-is.
WHAT WE MEASURE
Speed: FPS, average and slowest-5% frame time, CPU, RAM, temperature.
Quality: PCK@0.2, detection rate, jitter.
The first 30 frames of every Run are dropped as warm-up.
HOW ACCURACY IS SCORED
Accuracy is measured against Heavy running on the laptop, not against hand-labelled ground truth.
Those Reference landmarks are a stand-in. PCK@0.2 shows how closely a variant agrees with Heavy, so Heavy on the Board scores close to 100% by construction.
PASS CRITERIA FOR THE WEBCAM
On the Board, across all Clips:
• Average at least 10 FPS
• Slowest 5% of frames each 150 ms or less
• Person found in at least 90% of frames in Clips that contain one
• No crashes or out-of-memory Runs
We chose these ourselves, not from a standard. They can change if you name other targets.
LAPTOP BASELINE
All three variants also run on the laptop over the same Clips and are shown next to the Board's results.
Feedback wanted before we run it. Are these Pass criteria the right bar? Is Heavy an acceptable reference? Is anything missing from the comparison?
Notes: Early method check, sent before any full measurements run. Design reasoning is in the repo: ADR 0002 (why only the three Pose Landmarker variants), ADR 0003 (accuracy against Heavy as Reference landmarks, not ground truth), ADR 0004 (self-chosen Pass criteria). The natural next step for true accuracy is a labelled dataset such as Penn Action.